## Slide 1: Team OR Project Design Presentation
Jacob Breiholz Emilio Esteban Gabriel Ritter
ECE 3663 – Spring 2014
University of Virginia

## Slide 2: Design Description-ALU Layout
Notes: Values enter registers where they proceed to the operations. A mux selects the operation desired and passes it to the output register.

## Slide 3: Design Description (cont)
Bit slicing techniques were used for most components.
The function control points were assigned as seen at right.
Characteristic Inverter used:
NMOS and PMOS channel widths of 90nm
Function | Control (“S2,S1,S0”)
ADD | “000”
SUB | “001”
SHIFT | “010”
AND | “011”
OR | “100”
PASS | “101”
Multiply | “110”
NOP | “111”
Notes: If we were given information such as the probability that each operation would be called or the probability that certain functions would be called after a specific function then the order could make a significant difference because of static power and capacitor charging and discharging upon transitions.

## Slide 4: Adder Design
We decided to use a ripple carry configuration of mirror adders for our DSP
It is more efficient at propagating carries than a traditional FA, and will therefore will have less delay.
It uses less area than a typical CMOS FA, because it contains fewer inverters.

## Slide 5: Multiplier
Wallace Tree multiplier--an improvement over the common array multiplier
  O(log(N)) speed vs O(log2(n))
Helps the multiplier to work at speeds comparable to the rest of the DSP functions

## Slide 6: Shifter
3 columns of 16 single bit 2:1 muxes--Transmission gate muxes
First column shifts 1 bit, second column two bits, and third column 3 bits
(some combinational logic required)
Notes: The muxes were made using transmission gate logic. Since there are so many, this really cut down on size and power and also reduced delay
Need combinational logic since three selects needed but only two given.
Could have done columns differently but results this results in little combinational logic to select the number of shifts

## Slide 7: Sizing
Logical Effort was used to attempt to maximize the delay metric
The area cost alone from doing this was enough to make the overall metric worse, therefore most of the default sizes were preserved.
The clock buffer was ramped up to 2000x the characteristic inverter to improve transition times
Notes: clock buffer size has no limit since not part of metric and 4x load could be handled

## Slide 8: Results-Delay
Component | Delay (ps)
ADD | 533
SUB | 495
AND | 14.4
OR | 14.6
PASS | 15.1
SHIFT | 354
Multiplier | 298
Processor | 625

## Slide 9: Results-Power
Component | Power (W)
ADD | 4.09*10-5
SUB | 4.691*10-5
AND | 6.685*10-6
OR | 1.665*10-5
PASS | 2.299*10-11
SHIFT | 3.852*10-6
MUX | 1.572*10-5
Register | 1.115*10-4
Multiplier | 2.450*10-5
Processor | 2.503*10-4

## Slide 10: Results-Area
Component | Area (characteristic inverters)
ADD | 620
SUB | 620
OR | 48
AND | 48
PASS | 16
SHIFT | 160
8:1 16 bit MUX | 800
Register | 456
Multiplier | 2725
Total | 3730
Total Area (m):
6.714*10-4

## Slide 11: Results-Metric
The metric of our design is area*delay2*power. This comes out to be 6.56*10-26 m*s2*W
Also notable is the DSP’s ability to run on a 1.6GHz clock

## Slide 12: Conclusion
Design achieves full functionality
Design has maximum delay of 625ps even with more complex functions (i.e. multiplication)
Design has active power of 0.25mW per cycle
Design has total area of .67mm